## Slide 1: DNA sequencing, accuracy and errors
Linda van der Graaf – van Bloois
Faculty of Veterinary Medicine
Department of Biomolecular Health Sciences

## Slide 2
Haemophilus influenzae
1995
Entirely done by Sanger sequencing
Estimated cost: $0.48/base
> 1M€ per genome in todays money
Fleischmann et al Science. 1995 Jul 28;269(5223):496-512.
First microbial genome
Notes: I’ve sequenced Lactococcus lactis in 2002-2004. Took 2 years.

## Slide 3: Microbial sequencing projects
2015
Sanger sequencing
Chart: 
| 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
 | 1 | 4 | 6 | 20 | 50 | 70 | 100 | 150 | 170 | 250 | 300 | 500 | 700 | 1000 | 1500 | 2000 | 3000 | 4000 | 5000 | 6000
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 10 | 20 | 50 | 300 | 600 | 1000 | 2000 | 3000 | 5800
First bacteria:
H. influenzae
First mulicellular
organism: C. elegans
The global
ocean sampling
for metagenomics
Pyrosequencing
(454)
Next generation sequencing (NGS)
Complete genomes
Draft genomes
Microbial Sequencing projects
Rapid sequencing during EHEC outbreak
NCBI GenBank & SRA microbial genomes >10 million
1 genome
2 years
100k €/ genome
2016
2020
1000 genomes
6 weeks
<100 €/ genome

## Slide 4
2015
Third generation
Second generation
First generation

## Slide 5
Ion Gene S5
Ion Proton
Second generation (Short-read) sequencing methods
Roche 454
IonTorrent
Illumina
1st next-generation system: pyrosequencing
Discontinued
cheap, fast, sequence errors,
200-400 bp reads
Ion PGM
cheap, precise, slow, high-throughput, 50-300 bp reads
ISeq – MiniSeq - MiSeq
NextSeq – HiSeq – HiSeqX - NovaSeq

## Slide 6: Illumina sequencing
DNA sequencing depends on “reading” A/C/G/T signal
Signals: differently colored fluorophores

## Slide 7
Color signal of a cluster is not always 100% unambiguous
Illumina sequencing

## Slide 8
Illumina sequencing – quality scores bases
Phasing:
The blocker of a nucleotide is not correctly removed after signal detection
A nucleotide has a defect terminator cap (prephasing) and two nucleotides can bind in one cycle
Main reason for decreasing sequence quality:
Phasing
Decrease of fluorescent signal over time

## Slide 9
Phred 10: 10-1 chance that the base is wrong
  90% accuracy; 10% error rate
Phred 20: 10-2 chance that the base is wrong
  99% accuracy ; 1% error rate
Phred 30: 10-3 chance that the base is wrong
  99.9% accuracy ; 0.1% error rate
Quality scores
Notes: 9

## Slide 10: Phred score in ASCII text
Fastq quality score = Phred score -> converted to ASCII text

## Slide 11: Fastq files
Sequence and quality scores are stored in Fastq files
@NS500413:192:HCVY7AFXX:1:11101:10153:1038 1:N:0:AGTCAA
TGCACCCGCGTGATCGCGGTTTCCTGGGGCGCCACGGCGGCGGTCATCGGGCTGAACTGG
+
JJJJJJJFF/EAEEEAAAEEEE//EEEE/A<//<<<<6/<</<A<<AEAEE//AA6/<//
@NS500413:192:HCVY7AFXX:1:11101:19723:1039 1:N:0:AGTCAA
GGAAATGGAGTACGGATCGATTTTGTTTGG
+
JJJJJJJJJJJJJJJJ7FAEA715511E00
Every new entry starts with an “@” sign at the start of a line followed by an ID.
Fourth, the string of quality scores for each nucleotide is given on the fourth line.
Third, there is a line starting with +. This line can optionally contain the ID again.
The sequence is given on the second line.

## Slide 12: Phred scores in fastq files
@NS500413:192:HCVY7AFXX:1:11101:10153:1038 1:N:0:AGTCAA
TGCACCCGCGTGATCGCGGTTTCCTGGGGCGCCACGGCGGCGGTCATCGGGCTGAACTGG
+
JJJJJJJFF/EAEEEAAAEEEE//EEEE/A<//<<<<6/<</<A<<AEAEE//AA6/<//
@NS500413:192:HCVY7AFXX:1:11101:19723:1039 1:N:0:AGTCAA
GGAAATGGAGTACGGATCGATTTTGTTTGG
+
JJJJJJJJJJJJJJJJ7FAEA715511E00
Fourth, the string of quality scores for each nucleotide is given on the fourth line.
The sequence is given on the second line.
Phred score per base:
J = 74
74 – 33 = 41  phred score

## Slide 13: Fastq files
@NS500413:192:HCVY7AFXX:1:11101:10153:1038 1:N:0:AGTCAA
TGCACCCGCGTGATCGCGGTTTCCTGGGGCGCCACGGCGGCGGTCATCGGGCTGAACTGG
+
JJJJJJJFF/EAEEEAAAEEEE//EEEE/A<//<<<<6/<</<A<<AEAEE//AA6/<//
@NS500413:192:HCVY7AFXX:1:11101:19723:1039 1:N:0:AGTCAA
GGAAATGGAGTACGGATCGATTTTGTTTGG
+
JJJJJJJJJJJJJJJJ7FAEA715511E00
Illumina reads are all the same length when they come off the sequencer. If the sequences have different lengths, they have probably been processed.
Paired sequence and quality lines should be equally long.
The ID may contain information such as the run and the position of the cluster on the sequencing slide.
Sometimes the sample barcode is also listed.

## Slide 14: Fasta files
Sequences are stored in Fasta files
Fasta files are plain text files (open e.g. in )
>dna_sequence_A length=36 source=human_gut
CCGATCATATGACTAGCATGTCGACTAGCATTTAGA
>dna_sequence_B length=43 source=human_gut
GACTAGCATGCAATCGCGATAGCTATCGACTAGCATTTAGCGA
>dna_sequence_C length=86 source=human_gut
GCGGCGGCTAACGCATCGATCTTTGTACGATGATTGGCGGCGGC TATTATGCATTGGGAATGCATCGATCGACATCGATCGAAGCTAT
Every new entry starts with a “>” sign at the start of a line followed by an ID
Each ID is unique in the file. The ID is the part until a space, so no spaces allowed in the ID itself
While the description has to be on a single line, the sequence can be on one or more lines until the next “>” at the start of a line
There can be extra attributes or comments on the same line, but after the first space

## Slide 15
2015
Third generation
Second generation
First generation

## Slide 16: Third generation (Long-read) sequencing methods
Pacific Biosystems
(PacBio)
Oxford Nanopore
Technologies
Long reads (20 kb)
Perfect for genome assembly
Moderate to high error rate
Tiny (minION)
Long reads (>50 kb)
Perfect for genome assembly
High error rate
GridION
PromethION
SmidgION

## Slide 17: Oxford Nanopore
Jain et al. Nat Meth 2015
Open channel
DNA with molecular motor captured by nanopore
Translocation of 5’ adaptor
Translocation of template strand
Translocation of hairpin
Translocation of complement strand
Translocation of 3’ adaptor
Open channel
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
−
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Notes: Nucleotides have different sizes, which gives different currents in the nanopore

## Slide 18: Nanopore accuracy
By themselves, Nanopore sequences have relatively low accuracy (1D)
By measuring double stranded DNA, the same sequence can be measured twice (2D)
This decreases the error rate / increases accuracy
% identity to reference
Seemann, SlideShare 2015

## Slide 19: Homopolymer errors
Homopolymer: stretch of identical nucleotides
Homopolymer error: length is misidentified
  When longer than 3-5 nucleotides
  Problem with long-read sequencing
Longer homopolymer tracks: more errors
CCGTGTCAGCGGCATCGCCGGGGGGCAGGACATGAAGGCG
GTGTCAGCGGCATCGCCGGGGGGCAGGACATGAAGGCGGCGTG
TGTCAGCGGCATCGCCGGGGG-CAGGACATGAAGGCGAGTTGGGCAACCGG
TGTCAGCGGCATCGCCGGGGG-CAGGACATGAAGGCGGCGTGGGCAACCGGTGG
AGCGGCATCGCCGGGGGGCAGGACATGAAGGCGAGTTGGGCAACCGGTGG
GCGGCATCGCCGGGGGGCAGGACATGAAGGCGAGTTGGGCAACCGGTGGCA
CATCGCCGGGGG-CAGGACATGAAGGCGAGTTGGGCAACCGGTGGCATTGG
GCCGGGGG-CAGGACATGAAGGCGGCGTGGGCAACCGGTGGCATTGCCCTG

## Slide 20: Consensus correction
Long reads (Nanopore, Pacbio) can be corrected with shorter reads, or with contigs (e.g. Illumina)

## Slide 21
Summary
Second generation sequencing (Illumina)
Sequencing errors
Phred scores, fastq files
Third generation sequencing (Nanopore)
Homopolymer errors
Consensus correction